## Slide 1
Design and Simulation of an
18-DOF Walking Hexapod Robot
First Review
[Student names and roll numbers]
Guide: [Guide name]
Department of Mechanical Engineering, [Institution]

## Slide 2
Why a hexapod
Six legs make stability a geometry problem, not a control problem
• Wheels need continuous ground. Legs only need discrete places to put a foot.
• A robot is statically stable when its centre of mass projects inside the polygon of feet on the ground.
• Three points form a polygon, so a six legged robot can lift three legs and stay stable.
• That means stability can be checked geometrically instead of controlled continuously.
• A biped has no such margin and must balance every instant.
Consequence for this project
Static stability is an assertion we can write down and test offline, before any simulator is involved.
That is the basis of the whole verification approach in this project.

## Slide 3
Objectives for this phase
1
Accurate model
CAD to ROS 2 with measured masses and real inertia tensors, not placeholders
2
Inverse kinematics
Closed form solution for a 3-DOF leg, verified numerically
3
Walking gait
Tripod gait from a commanded velocity, verified for stability and non-slip
4
Control integration
ros2_control, so the same interface works in simulation and on hardware
5
Demonstration
Robot walking in simulation under operator control
6
Hardware ready
Architecture where moving to servos is a configuration change

## Slide 4
The robot
Six legs, three joints each, built from our own CAD
Component | Length (mm) | Mass (kg)
Body | 312.7 x 283.3 | 1.310
Coxa | 150.0 | 0.201
Femur | 116.6 | 0.101
Tibia | 150.0 | 0.035
Masses come from measured mesh volumes at PLA density. Each servo's mass belongs to the link it is bolted to, not the link it drives.
Mass ratios across a joint matter more than absolute values. One link fifty times wrong relative to its neighbour is what makes a simulated robot fly apart.
18
actuated joints
25
links
3.39
kg total
6
legs

## Slide 5
Software architecture
Five packages. Each boundary stops one kind of change spreading
Package | Why it is separate
hexapod_description | Model, meshes. Data only. Must be usable without a simulator dependency
hexapod_gazebo | World and physics. Delete it and the stack still runs on hardware
hexapod_control | Controller config, swapped wholesale between sim and hardware
hexapod_gait | Kinematics and gait. The mathematics, deliberately separable from ROS
hexapod_bringup | Launch files. Nothing depends on it, so it can change freely
hexapod_description depends on nothing at all. That single property is what makes hardware integration next phase a configuration change rather than a rewrite.

## Slide 6
One input, everything else derived
No motion is scripted and nothing is a recorded animation
Velocity command
the only input
›
Gait generator
50 Hz, foot position for each leg
›
Inverse kinematics
six foot positions to 18 joint angles
›
Controller manager
200 Hz, inside the Gazebo process
›
Physics
1000 Hz
Ask for a different velocity and every leg trajectory changes. The controller manager runs inside the Gazebo process on purpose, because the control loop has to run in step with the physics rather than asynchronously over a network.

## Slide 7
Inverse kinematics
A 3D problem that collapses to 2D, so it has an exact solution
• The femur and tibia rotate about the same axis direction, so everything past the coxa lies in one vertical plane.
• The coxa angle only selects which plane. Three dimensions become two.
• A two link planar reach has an exact answer by the law of cosines. No numerical solver, so nothing can fail to converge.
• The law of cosines gives two valid answers, both placing the foot in the same spot but folding the leg differently.
Choosing the elbow
Knee 136 mm inside the foot
1.48 N m at the knee
Knee 18 mm inside the foot
0.19 N m at the knee
Same foot position, nearly 8x the load. The first choice made the tibia sag 24 degrees.
A simulation number leading directly to a mechanical decision, including a servo horn offset at assembly.

## Slide 8
Tripod gait
Stride length is derived from the commanded velocity, never tuned
• Two groups of three legs, exactly half a cycle out of phase. Three feet down at every instant.
• A planted foot must not move relative to the ground, but we command foot positions in the body frame.
• So a stationary foot must travel backwards through the body frame at exactly the body speed.
• Stride is therefore forced by the velocity and the stance duration. It is not a free parameter.
• Each leg gets a different stride when turning, because a point further from the turn centre travels further.
One expression covers
• walking forwards
• walking backwards
• strafing sideways
• turning on the spot
• driving an arc
Which is why these are one code path rather than five special cases.

## Slide 9
What verification found
A sign error that visual inspection could never have caught
The fault
The stance phase swept each foot forwards through the body frame instead of backwards. The stride vector already pointed backwards, and the formula negated it a second time.
Commanded 0.08 m/s forward, we measured the planted foot being dragged over the ground at 0.16 m/s, in the wrong direction, on three legs at once.
The legs were pushing the robot backwards while the gait believed it was going forwards.
Why our own test passed
The non-slip check compared the distance the foot travelled against the distance the body travelled.
Both are distances. A distance has no direction, so a sign error is invisible to it.
The test was checking the right property with the wrong operator, and would have passed indefinitely. It is now a signed vector comparison.
Found by comparing our sign conventions against an independently written hexapod stack.

## Slide 10
Verification before simulation
The kinematics and gait have no ROS dependency, so they test in under a second
3.5e-16 m
worst inverse kinematics round trip error
498
gait assertions passing
32
kinematics assertions passing
What the gait suite checks
Exactly three feet down at every sampled phase. Tripod groups exactly half a cycle apart. No positional jump at the stance and swing handover. Stance foot velocity zero relative to the ground. Full 45 mm swing clearance. Stance travel matching body travel in size and direction. Every velocity in the allowed envelope reachable within joint limits.
A phase is not finished because code was written. It is finished when a stated check passes.

## Slide 11
Three simulation configurations compared
Each commanded forward at 0.03 m/s for 20 s, measured from ground truth
Configuration | Body travel | Tracking | Result
Position interface, measured model | 0.4 mm | 0 % | Legs cycle correctly, body does not move
Effort interface, light model | 0.59 m | 99 % | Walks, but rises 5 cm and tilts 12 degrees
Effort interface, measured model | not measured | not measured | Body stays at the origin, unresolved
Why position control cannot walk
Gazebo carries out a position command by relocating the joint without giving it a velocity. Contact friction is computed from sliding velocity, so the solver sees a stationary foot and generates no propulsion. The controller tracked its commands to four decimal places. It did exactly what it was told and the physics still produced no motion.
The light model walks because it is not physical. At 0.00001 kg per link, gravity torque is negligible and a crude controller has far more authority than it needs.

## Slide 12
Demonstration
Kinematic simulation. Leg trajectories come from the gait generator and the analytic inverse kinematics, with nothing animated.
The body displacement is what those trajectories geometrically require, because the gait is provably non-slip.
Forward, reverse, strafe, turn both directions, and an arc.

## Slide 13
Status and what is unfinished
Complete
• CAD converted to a ROS 2 model
• Masses, inertias, collision, friction
• Spawns and stands in Gazebo
• ros2_control, all controllers active
• All 18 joints verified individually
• Inverse kinematics, verified
• Tripod gait, verified
• Teleoperation and walking demonstration
Not finished
Walking under full dynamics with the measured model. Characterised but not solved.
Effort control gains untuned. A velocity feedforward parameter is silently rejected because its format changed between ROS 2 releases, so that term is currently inactive.
Hardware interface exists as architecture only. No servo driver written yet.

## Slide 14
Next phase
1
Find the cause of the fixed base under effort control
2
Fix the feedforward parameter format, then tune the effort gains
3
Enable per foot contact sensors to measure slip directly instead of inferring it
4
Write the servo driver and assemble the physical robot
5
Add mapping and navigation, for which the architecture already leaves room
The gait, the kinematics and the model do not need to change for any of this.